## Slide 1
CSE207 · Digital Logic Design
Class 2: Boolean Algebra and Boolean Expressions
Masnoon Muztahid
Lecturer
Department of Computer Science and Engineering
Presidency University
Notes: Welcome back. Class 1 ended by naming today's topic: Boolean algebra and Boolean expressions.

## Slide 2
RECAP
Where We Left Off in Class 1
CSE207 · Digital Logic Design · Class 2
2 / 26
FROM CLASS 1
Digital logic uses only two values: 0 and 1. A logic gate takes binary inputs and produces a binary output. A truth table lists every input combination together with the output.
AND
1 only if BOTH inputs are 1
OR
1 if AT LEAST ONE input is 1
NOT
flips the input value
COMING BACK LATER
NAND, NOR, XOR and XNOR were introduced in Class 1. We will revisit them when we need them.
Notes: Keep this short - three minutes. The only goal is to bring back 0/1, gates and truth tables.

## Slide 3
INTRODUCTION
What Will We Learn Today?
CSE207 · Digital Logic Design · Class 2
3 / 26
Boolean Values
Boolean Operations
Boolean Expressions
Expression → Circuit
Expression → Truth Table
Simplification
By the end of this class, you will be able to:
1
Use 0 and 1 as Boolean values
2
Apply the AND, OR and NOT operations
3
Read and write Boolean expressions
4
Turn an expression into a logic circuit
5
Build a truth table for a whole expression
6
Simplify expressions using Boolean laws
Notes: Show the road map on the left; read the six objectives on the right.

## Slide 4
BOOLEAN VALUES
Boolean Values: Only 0 and 1
CSE207 · Digital Logic Design · Class 2
4 / 26
NEW TERM
Boolean algebra — the mathematics of values that can only be 0 or 1. It is the language we use to describe what a digital circuit does.
0
FALSE
also read as: no · OFF · LOW
1
TRUE
also read as: yes · ON · HIGH
IMPORTANT
A Boolean variable (A, B, C …) is simply a name for a value that is either 0 or 1 — there is nothing in between.
In Class 1, 0 and 1 were voltage levels. From now on they are values we can calculate with.
Notes: Class 1 treated 0 and 1 as voltage levels. Today they become values we can calculate with.

## Slide 5
BOOLEAN OPERATIONS
The Three Boolean Operations
CSE207 · Digital Logic Design · Class 2
5 / 26
AND
read as “A AND B”
1 only if BOTH inputs are 1
A | B | F
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
OR
read as “A OR B”
1 if AT LEAST ONE input is 1
A | B | F
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
NOT
read as “NOT A”
flips the value it is given
A | F
0 | 1
1 | 0
THE LINK BACK TO CLASS 1
Each Boolean operation is exactly what one of the gates already does: AND → AND gate, OR → OR gate, NOT → NOT gate.
Notes: Same three operations as the three basic gates in Class 1 - now written as mathematics.

## Slide 6
BOOLEAN OPERATIONS
Careful: “+” Means OR, Not Addition
CSE207 · Digital Logic Design · Class 2
6 / 26
IMPORTANT
In Boolean algebra “+” means OR and “ · ” means AND. They are logic operations, not arithmetic.
because 1 OR 1 = 1
COMPARE
Arithmetic: 1 + 1 = 2
Boolean: 1 + 1 = 1
ORDER OF OPERATIONS
NOT is applied first, then AND ( · ), then OR ( + ) — exactly as × comes before + in ordinary arithmetic. Use brackets whenever you want a different order.
A Boolean result is always 0 or 1 — never 2.
Notes: This is the single most common beginner mistake. Spend a minute on 1 + 1 = 1.

## Slide 7
BOOLEAN EXPRESSIONS
What Is a Boolean Expression?
CSE207 · Digital Logic Design · Class 2
7 / 26
NEW TERM
Boolean expression — a combination of Boolean variables and Boolean operations that produces a Boolean result (0 or 1).
EXAMPLES
HOW TO READ ONE
1
First do A AND B
2
Then OR that result with C
“ · ” is done before “ + ”, just like × before +.
An expression says exactly how the output is built from the inputs.
Notes: Read each example aloud in words before moving on.

## Slide 8
EXPRESSION → CIRCUIT
From an Expression to a Circuit
CSE207 · Digital Logic Design · Class 2
8 / 26
Every operation in the expression becomes one gate in the circuit.
one AND gate
one OR gate
one NOT gate
RULE OF THUMB
Find the operations in the expression, draw one gate for each of them, then connect the gates in the order the expression is evaluated.
Notes: One operation = one gate. Start from the smallest possible examples.

## Slide 9
EXPRESSION → CIRCUIT
Building a Circuit Step by Step
CSE207 · Digital Logic Design · Class 2
9 / 26
STEP 1
AND A with B — that gives A · B.
STEP 2
OR that result with C. That gives the whole expression.
The AND is evaluated first, so the AND gate comes first in the circuit.
Circuit for F = A · B + C
Two operations → two gates. The AND gate's output becomes an input of the OR gate.
Notes: Draw this on the board at the same time as the slide.

## Slide 10
EXPRESSION → CIRCUIT
Adding a NOT Gate
CSE207 · Digital Logic Design · Class 2
10 / 26
WHAT CHANGED?
C now has a bar over it. The bar means NOT C, so a NOT gate is placed on the C line before the OR gate.
READ IT AS
NOT C first, then A AND B, then OR the two results together.
One AND gate, one NOT gate and one OR gate.
A bar over a variable always becomes a NOT gate in the circuit.
Notes: Point at the bar over C, then at the NOT gate on the C line.

## Slide 11
EXPRESSION → TRUTH TABLE
A Truth Table for a Whole Expression
CSE207 · Digital Logic Design · Class 2
11 / 26
In Class 1 we built truth tables for single gates. Now we build one for a complete expression.
A | B | F = A + B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
The OR gate and the expression A + B give exactly the same table.
HOW MANY ROWS?
For n input variables the table has 2ⁿ rows — one row for every possible combination of inputs.
Inputs (n) | Rows (2ⁿ)
1 | 2¹ = 2
2 | 2² = 4
3 | 2³ = 8
Count 00, 01, 10, 11 … like counting in binary, so no row is missed or repeated.
Notes: Class 1 built truth tables for single gates. Now we do it for a complete expression.

## Slide 12
EXPRESSION → TRUTH TABLE
Using Intermediate Columns
CSE207 · Digital Logic Design · Class 2
12 / 26
WHY AN EXTRA COLUMN?
Do not try to work out F in one jump. First find A · B, then OR it with C.
1
Fill in A, B and C — all 8 combinations
2
Work out A · B in each row
3
Then F = (A · B) + C
3 variables → 2³ = 8 rows.
The extra column turns one hard step into two easy ones.
A | B | C | A · B | F = A · B + C
0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 1
0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1
1 | 0 | 0 | 0 | 0
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1
1 | 1 | 1 | 1 | 1
Highlighted row: A · B is 1, so F is 1 even though C = 0.
Notes: Stress this: never try to get F in one jump. Add a column for each inner term.

## Slide 13
BIG IDEA
Three Representations of the Same Logic Function
CSE207 · Digital Logic Design · Class 2
13 / 26
BOOLEAN EXPRESSION
the mathematics
LOGIC CIRCUIT
the hardware
TRUTH TABLE
the behaviour
A | B | C | F
0 | 0 | 0 | 0
0 | 0 | 1 | 1
0 | 1 | 0 | 0
0 | 1 | 1 | 1
1 | 0 | 0 | 0
1 | 0 | 1 | 1
1 | 1 | 0 | 1
1 | 1 | 1 | 1
↔
↔
Three different views — one and the same logic function. You can move between them in any direction.
Notes: This is the central idea of Class 2. Make sure everyone sees that all three describe one function.

## Slide 14
WHY SIMPLIFY?
Why Do We Simplify Boolean Expressions?
CSE207 · Digital Logic Design · Class 2
14 / 26
Look at this expression — the same term is written twice.
BEFORE
2 AND gates + 1 OR gate
AFTER
1 AND gate
Idempotent Law: A + A = A
Fewer gates can mean less hardware, less area and less delay.
Different expressions can describe the same logic function — but one of them may need a simpler circuit.
Notes: Ask the class what they notice before revealing the right-hand card.

## Slide 15
BOOLEAN LAWS
Boolean Algebra Laws — Part 1
CSE207 · Digital Logic Design · Class 2
15 / 26
These laws are tools. We use them to rewrite an expression into a simpler one.
IDENTITY LAW
0 in an OR and 1 in an AND change nothing.
NULL LAW
1 in an OR and 0 in an AND decide the result on their own.
IDEMPOTENT LAW
Repeating a term adds nothing new.
COMPLEMENT LAW
A variable and its opposite cover everything, or nothing.
INVOLUTION LAW
Two NOTs cancel each other out.
HOW TO USE THEM
You do not have to memorise these. Learn to recognise the pattern, then look the law up while you simplify.
Notes: Do not ask anyone to memorise these today. They are tools to recognise, not facts to recite.

## Slide 16
BOOLEAN LAWS
Boolean Algebra Laws — Part 2
CSE207 · Digital Logic Design · Class 2
16 / 26
These laws let us re-order, re-group and factor an expression.
COMMUTATIVE LAW
The order of the terms does not matter.
ASSOCIATIVE LAW
The grouping of the terms does not matter.
DISTRIBUTIVE LAW
Multiply out, or factor back in. Note the second form — it has no arithmetic twin.
ABSORPTION LAW
The bigger term already covers the smaller one.
MOST USED TODAY
Absorption, Complement, Identity and Distributive are the four laws that do most of the work when we simplify.
REMEMBER
A law is only a rewrite. The expression looks different afterwards, but the output for every input stays the same.
Notes: Absorption and Distributive are the two we will actually use in today's examples.

## Slide 17
BOOLEAN LAWS
Checking a Law with a Truth Table
CSE207 · Digital Logic Design · Class 2
17 / 26
You never have to trust a law. If both sides give the same output in every row, the law is correct.
IDENTITY LAW
A | 0 | A + 0
0 | 0 | 0
1 | 0 | 1
The last column is identical to the A column, so A + 0 = A.
IDENTITY LAW
A | 1 | A · 1
0 | 1 | 0
1 | 1 | 1
Again the last column matches A, so A · 1 = A.
Same output in every row means the same logic function. That is the whole proof.
Notes: Show them they never have to take a law on trust.

## Slide 18
DE MORGAN'S LAWS
De Morgan's Laws
CSE207 · Digital Logic Design · Class 2
18 / 26
LAW 1
LAW 2
ONE TRUTH TABLE PROVES BOTH LAWS
A | B | A + B |  |  | A · B |  | 
0 | 0 | 0 | 1 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 0 | 1 | 1
1 | 0 | 1 | 0 | 0 | 0 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1 | 0 | 0
LAW 1 — these two match
LAW 2 — these two match
EASY WAY TO REMEMBER
Break the bar, change the operation — and every variable gets its own bar.
NEXT CLASS
These laws become especially useful when we build circuits out of NAND and NOR gates.
Notes: Say the memory rule out loud twice: break the bar, change the operation. Then walk the class along one row of the table at a time - the A+B and A.B columns are the intermediate columns, and the two bracketed pairs are what actually prove the laws.

## Slide 19
SIMPLIFICATION
Simplifying Step by Step
CSE207 · Digital Logic Design · Class 2
19 / 26
EXAMPLE 1
given
The term A already covers A · B, so A · B adds nothing new.
Absorption Law
Whenever you see A + A · B, the answer is simply A.
THE LAW USED
EXAMPLE 2
given
factor out A
Complement Law
Identity Law
Every step is allowed because a Boolean law says so.
The expression changes at every step — the logic function does not.
Notes: Name the law out loud at every single step. That is the habit we want.

## Slide 20
DE MORGAN'S LAWS
Simplifying with De Morgan's Laws
CSE207 · Digital Logic Design · Class 2
20 / 26
EXAMPLE 1
given
De Morgan's Law
Distributive Law
Complement + Identity
EXAMPLE 2
given
De Morgan's Law
Distributive Law
Null + Identity
EXAMPLE 3
given
De Morgan's Law
Absorption Law
Every De Morgan simplification starts the same way: break the bar, then apply the ordinary laws.
Notes: Three-variable examples. In every one the FIRST move is De Morgan - break the bar - and only then do the ordinary laws apply. Point that out each time. Ex 1 ends on Complement, Ex 2 on Null (A-bar + 1 = 1), Ex 3 on Absorption.

## Slide 21
SIMPLIFICATION
Same Logic Function, Simpler Circuit
CSE207 · Digital Logic Design · Class 2
21 / 26
BEFORE SIMPLIFICATION
2 AND gates, 1 OR gate, 1 NOT gate
4 gates
AFTER SIMPLIFICATION
No gates at all — the output simply follows A.
Factor out A, then B + NOT B = 1, then A · 1 = A.
0 gates
Both circuits have exactly the same truth table. Boolean algebra changes the hardware, not the logic.
Notes: This is where Boolean algebra stops being maths and becomes hardware.

## Slide 22
SIMPLIFICATION
A Harder Example: Three Variables
CSE207 · Digital Logic Design · Class 2
22 / 26
STEP BY STEP
given
factor out A
Complement Law
Identity Law
CIRCUIT FOR THE SIMPLIFIED EXPRESSION
2 gates instead of 6 (1 NOT, 3 AND, 2 OR).
TRUTH TABLE — 8 ROWS FOR 3 VARIABLES
A | B | C |  | A · B | B · C | F | A + B · C
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0 | 0 | 1 | 0 | 0 | 0 | 0 | 0
0 | 1 | 0 | 0 | 0 | 0 | 0 | 0
0 | 1 | 1 | 0 | 0 | 1 | 1 | 1
1 | 0 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 1
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1
1 | 1 | 1 | 0 | 1 | 1 | 1 | 1
The F column and the A + B · C column match in every row — the simplification is correct.
Same logic function — 6 gates or 2. Boolean algebra decides which.
Notes: Everything from today in one problem. Work the three parts on the board in this order: simplify, draw the simplified circuit, then check with the truth table. The key move is spotting that the first two terms share A.

## Slide 23
PRACTICE
Your Turn
CSE207 · Digital Logic Design · Class 2
23 / 26
1
Simplify
Hint: Idempotent Law.
2
Simplify
Hint: Absorption Law.
3
Simplify
Hint: factor out A first.
MINI CHALLENGE
Try this one yourself before looking at the next slide.
Hint: use the Distributive Law in the form A + B · C = (A + B) · (A + C).
Take two or three minutes. The answers are on the next slide.
Notes: Give them two or three minutes. Walk around; do not reveal the answers early.

## Slide 24
PRACTICE
Answers
CSE207 · Digital Logic Design · Class 2
24 / 26
Q1
Idempotent Law A + A = A
Q2
Absorption Law A + A · B = A
Q3
Complement + Identity Laws
MINI CHALLENGE — SOLUTION
1
given
2
Distributive Law
3
Complement Law
4
Identity Law
Notice that every single step is justified by a named Boolean law.
Notes: Make the law name the point of each answer, not the letter A.

## Slide 25
HOMEWORK
Homework
CSE207 · Digital Logic Design · Class 2
25 / 26
FOR EACH EXPRESSION BELOW, DO ALL THREE
1
Simplify the expression
2
Draw the simplified circuit
3
Build the truth table
EXPRESSIONS
1
2
3
4
5
6
7
8
Name the law you used at every step. Warm-up (no circuit needed): simplify A + 0 and A · 1.
Hints — for 6 start with De Morgan; for 8, two factors that differ only in C collapse into one.
Simplification is a skill — it only comes with practice.
Notes: Answers. 1) A Absorption. 2) A factor A, Complement, Identity. 3) A + B Distributive, Complement, Identity. 4) A.B factor A.B, then C + NOT C = 1, Identity. 5) A.(B + C) Absorption removes A.B.C, then factor A. 6) A De Morgan and Involution turn the first factor into A + B, then (A+B)(A+NOT B) = A + B.NOT B = A. 7) C.(A + B) factor A.C from the first two terms, then A.C + NOT A.B.C = C.(A + NOT A.B) = C.(A + B). 8) A the first two factors give (A+B) + C.NOT C = A + B, then (A+B)(A+NOT B) = A. Truth-table sizes: 1, 2, 3 and 6 are two-variable, so 4 rows; 4, 5, 7 and 8 are three-variable, so 8 rows. Problems 6 to 8 are the hard ones - warn the class that they need more than one law each.

## Slide 26
BIG PICTURE
The Big Picture
CSE207 · Digital Logic Design · Class 2
26 / 26
Boolean Values · 0 and 1
Boolean Operations
Boolean Expressions
Circuit + Truth Table
Boolean Laws · De Morgan
Simpler Circuit
KEY TAKEAWAYS
1
Boolean variables have only two values: 0 and 1.
2
A Boolean expression describes a logic function.
3
The same function can be shown as an expression, a circuit or a truth table.
4
Boolean laws let us rewrite an expression into a simpler one.
5
A simpler expression can mean a simpler circuit — with the same output.
Next question: can we build any circuit using only ONE type of gate?
Next class: Universal Gates — NAND and NOR
Notes: Close the loop back to Class 1, then open the door to Class 3.