## Slide 1
CSE322
Microprocessors Based System Design Laboratory
CLASS 1
Introduction to Microprocessors and Basic CPU Organization
Masnoon Muztahid
Lecturer, Department of Computer Science and Engineering
Presidency University
Co-requisite: CSE321 · Credits: 01
CPU
on a single chip

## Slide 2
COURSE ROADMAP
Where Are We Going?
CSE322 · Class 1 · Introduction to Microprocessors
2
TODAY · Class 1
1
Computer Basics
2
Microprocessor Fundamentals
3
SAP-1: a simple computer model
4
8086 Architecture
5
8086 Assembly Language
6
Arithmetic & Logic
7
Bit Manipulation
8
Branching & Loops
9
Arrays & Strings
10
Memory & I/O Interfacing
Today we start from the fundamentals. Every later class builds on today's ideas.

## Slide 3
CLASS 1 GOALS
Today's Learning Objectives
CSE322 · Class 1 · Introduction to Microprocessors
3
By the end of today's class, you will be able to...
1
Explain what a computer and a CPU (processor) do
2
Tell the difference between a microprocessor and a microcontroller
3
Name the three main parts of a CPU: ALU, Control Unit and Registers
4
Explain why a CPU needs memory and buses
5
Describe what an instruction is
6
Walk through the Fetch → Decode → Execute cycle
7
Explain how SAP-1, a simple model computer, runs an instruction
Why? These ideas are the foundation for understanding and programming the Intel 8086.

## Slide 4
PART 1 · THE BIG PICTURE
What Does a Computer Do?
CSE322 · Class 1 · Introduction to Microprocessors
4
INPUT
Data entering the computer
PROCESSING
Working on the data: calculate, compare, decide
OUTPUT
Results leaving the computer
EXAMPLES
You press the key “A”
Recognises which key was pressed
“A” appears on the display
You click on a file icon
Works out what the click means
The file opens on the screen
Key idea: Processing is mainly performed by the CPU (Central Processing Unit). Let's look inside.

## Slide 5
PART 1 · THE BIG PICTURE
What is a CPU / Processor?
CSE322 · Class 1 · Introduction to Microprocessors
5
WHAT
Central Processing Unit (CPU), also called the processor: the part of a computer that executes instructions and processes data.
Instructions
e.g. “add two numbers”
Data
e.g. the numbers 5 and 3
CPU
executes & processes
Result
e.g. 8
1 RECEIVES
instructions and data (from memory)
2 PROCESSES
them: calculates, compares, moves data
3 PRODUCES
results: stored or sent to an output device

## Slide 6
PART 1 · THE BIG PICTURE
What is a Microprocessor?
CSE322 · Class 1 · Introduction to Microprocessors
6
WHAT
Microprocessor: a CPU built on a single integrated circuit (IC) chip.
Integrated circuit = a tiny silicon chip holding thousands to billions of tiny electronic switches (transistors). Why it matters: a whole CPU on one small, cheap chip made personal computers possible.
Microprocessor
Microcontroller
THIS COURSE
CPU
Memory chip
I/O chip
CPU
Memory
I/O
Chip contains only the CPU; memory and I/O (input/output) are separate chips
Used in general-purpose computers: PCs, laptops
Examples: Intel 8086, Intel Core i5
CPU + memory + I/O all on one chip: a “computer on a chip”
Used in dedicated devices: microwave, washing machine, TV remote
Examples: 8051, ATmega328P (Arduino Uno)

## Slide 7
PART 2 · CPU FUNDAMENTALS
Inside a CPU: Three Main Parts
CSE322 · Class 1 · Introduction to Microprocessors
7
CPU
Control Unit
Registers
ALU
control signals
data
Arithmetic Logic Unit (ALU)
Performs arithmetic operations (add, subtract) and logical operations (AND, OR, NOT, compare).
Control Unit (CU)
Coordinates and controls instruction execution: tells every part what to do, and when.
Registers
Small, very fast storage locations inside the CPU that hold the data being worked on.
Next three slides: a closer look at each part.

## Slide 8
PART 2 · CPU FUNDAMENTALS
ALU: The Calculator of the CPU
CSE322 · Class 1 · Introduction to Microprocessors
8
WHAT
Arithmetic Logic Unit (ALU): the CPU part that performs arithmetic and logic operations.
Why? Every calculation or comparison in a program is done by the ALU.
Register A
5
Register B
3
ALU
Result register
8
Control Unit
says “ADD”
ARITHMETIC
ADD: 5 + 3 = 8
SUBTRACT: 9 − 4 = 5
LOGIC
AND, OR, NOT: work on bits (0s and 1s)
COMPARE: Is 5 > 3? → Yes
Registers hold the operands (input values 5 and 3) and the result (8). The ALU only does the work. The 8086 also has an ALU (for 16-bit numbers).

## Slide 9
PART 2 · CPU FUNDAMENTALS
Registers: The CPU's Fast Temporary Storage
CSE322 · Class 1 · Introduction to Microprocessors
9
WHAT
A register is a small, very fast storage location inside the CPU. A CPU has only a few of them.
WHY
The CPU needs somewhere very close by to hold data and intermediate results while it executes instructions.
EXAMPLE
To compute 5 + 3, the CPU keeps 5 and 3 in registers, the ALU adds them, and 8 is placed in a register.
NEXT CLASS
The 8086 has registers named AX, BX, CX and DX. We will study them in the next class.
REGISTERS
Inside the CPU · very fast · very small (only a few)
≈ the items on your desk
vs
MEMORY (RAM)
Outside the CPU · slower than registers · much larger (billions of locations)
RAM = Random Access Memory, the computer's main memory
≈ a big storage cabinet
Analogy for intuition only: you keep what you are using right now close at hand.

## Slide 10
PART 2 · CPU FUNDAMENTALS
Control Unit: The Coordinator
CSE322 · Class 1 · Introduction to Microprocessors
10
WHAT
Control Unit (CU): coordinates the activities of the CPU. It reads each instruction and sends control signals telling the other parts what to do, and when.
Control signal = an on/off electrical signal that commands a component (e.g. “read”, “add”). Why? Without it, the parts would not act in the right order.
Instruction
e.g. ADD
Control Unit
Memory “Send a value”
Registers “Hold this number”
ALU “Perform ADD now”
ANALOGY
Like a traffic controller: it drives no car itself, but tells each one when to go and when to stop.
(for intuition only)
QUICK CHECK: Which CPU part performs addition? And which part tells it when to add?

## Slide 11
PART 3 · MEMORY, BUSES AND INSTRUCTIONS
CPU + Memory: Where Programs Live
CSE322 · Class 1 · Introduction to Microprocessors
11
CPU
read / write
Address | Contents | Type
0 | ADD | Instruction
1 | 5 | Data
2 | 3 | Data
3 | 8 | Result
Memory
WHAT
Memory stores the instructions and data that the CPU works with.
Address = the number of each memory location (like a house number).
Instructions
what to do
Data
what to work on
Results
what was produced
WHY
Registers hold only a few values. A program needs a much bigger place for all its instructions and data.
EXAMPLE
To compute 5 + 3, the instruction (ADD) and the numbers (5, 3) must be in memory. The result (8) can be written back.
THINK: The CPU and memory are separate parts. How does information travel between them?

## Slide 12
PART 3 · MEMORY, BUSES AND INSTRUCTIONS
What is a Bus?
CSE322 · Class 1 · Introduction to Microprocessors
12
WHAT
Bus: a group of parallel wires (a shared pathway) that transfers information between components.
Why? The CPU, memory and input/output (I/O) devices are separate parts and need a pathway to exchange information.
CPU
Memory
Input / Output
BUS (shared pathway)
Example: when the CPU needs the number 5 from memory, the 5 travels from memory to the CPU along the bus.
THREE TYPES OF BUS · DETAILS ON THE NEXT SLIDE
Data Bus carries the data
Address Bus carries the location
Control Bus carries the commands
8086 link: the 8086 has a 16-bit data bus (moves 16 bits at once) and a 20-bit address bus.

## Slide 13
PART 3 · MEMORY, BUSES AND INSTRUCTIONS
Three Types of Bus
CSE322 · Class 1 · Introduction to Microprocessors
13
CPU
Memory
ADDRESS BUS “location 1”
DATA BUS the value 5
CONTROL BUS “READ”
Example: the CPU reads the value 5 from memory location 1
ADDRESS BUS
Carries: the address of the memory location the CPU wants to use
Direction: CPU → memory (one way)
Analogy: “Which house?”
DATA BUS
Carries: the actual data or instruction being moved
Direction: both ways (CPU ↔ memory)
Analogy: “What is being delivered?”
CONTROL BUS
Carries: control signals such as READ and WRITE
Direction: mostly from the CPU
Analogy: “What should happen?”
THINK: What is the difference between an address and data? (Hint: “which house?” vs “what is inside?”)

## Slide 14
PART 3 · MEMORY, BUSES AND INSTRUCTIONS
What is an Instruction?
CSE322 · Class 1 · Introduction to Microprocessors
14
WHAT
Instruction: a single command that tells the processor what operation to perform.
Program = a sequence of instructions stored in memory. The CPU runs them one by one.
LOAD
Copy data from memory into a register
ADD
Add two numbers using the ALU
STORE
Copy a result from a register into memory
COMPARE
Check if two values are equal, or which is bigger
EXAMPLE PROGRAM: compute 5 + 3
1 LOAD 5
2 ADD 3
3 STORE result
→ put 5 in a register
→ 5 + 3 = 8
→ save 8 in memory
Inside the computer, every instruction is a binary number (0s and 1s, e.g. 0001 1010), called machine code. Humans write them as short words like ADD: this is assembly language.
Later classes: we will write instructions in 8086 assembly language.

## Slide 15
PART 4 · THE INSTRUCTION CYCLE
How Does the CPU Execute an Instruction?
CSE322 · Class 1 · Introduction to Microprocessors
15
FETCH
DECODE
EXECUTE
repeat for every instruction
Instruction cycle: the steps the CPU repeats for every instruction.
1
FETCH: Get the next instruction from memory.
e.g. bring “ADD” into the CPU
2
DECODE: Work out what the instruction means.
e.g. “ADD” means: add two numbers
3
EXECUTE: Perform the required operation.
e.g. the ALU adds the numbers
Analogy: following a recipe: read the step → understand it → do it → next step.

## Slide 16
PART 4 · THE INSTRUCTION CYCLE
Example: Executing a Simple Addition
CSE322 · Class 1 · Introduction to Microprocessors
16
Instruction: “ADD 5 and 3”
FETCH
DECODE
EXECUTE
1
FETCH
“ADD 5, 3”
The CPU gets the instruction from memory.
2
DECODE
ADD = add
The Control Unit works out that addition is required.
3
GET DATA
5 and 3
The numbers are brought into registers.
4
EXECUTE
5 + 3
The ALU performs the addition.
5
RESULT
8
The result is stored in a register or memory.
WHO DOES IT?
Memory → bus → CPU
Control Unit
Memory → registers
ALU
Register / memory
THINK: What are the three stages of the instruction cycle? Say them in order without looking.

## Slide 17
PART 5 · SAP-1: A SIMPLE COMPUTER
Why Do We Study SAP-1?
CSE322 · Class 1 · Introduction to Microprocessors
17
Problem: a real processor such as the 8086 has many parts and features. Learning everything at once is hard.
WHAT
SAP-1 (Simple-As-Possible computer 1): a simplified educational computer, designed only for teaching, that contains just the essential parts of a CPU.
SAP-1
simple model · 8-bit · 16 memory locations · 5 instructions
builds intuition
Intel 8086
real processor · 16-bit · 1 MB of memory · 100+ instructions
SAP-1 HELPS US UNDERSTAND
Registers
Memory
Bus
ALU
Control Unit
Instruction execution
THINK: Why do learner drivers practise in an empty parking lot before driving in city traffic?

## Slide 18
PART 5 · SAP-1: A SIMPLE COMPUTER
SAP-1: The Big Picture
CSE322 · Class 1 · Introduction to Microprocessors
18
BUS
Program Counter (PC)
Points to the next instruction
Memory
Stores instructions and data
Instruction Register (IR)
Holds the current instruction
Accumulator (ACC)
Holds data and results for the ALU
ALU
Adds or subtracts
Control Unit
Decodes and sends control signals
How to read this diagram
1
Every block connects to one shared bus.
2
At any moment, one block sends information on the bus and another block receives it.
3
The Control Unit decides who sends and who receives, step by step.
Simplified view: the real SAP-1 also has a memory address register, a B register and an output register.

## Slide 19
PART 5 · SAP-1: A SIMPLE COMPUTER
Important SAP-1 Components
CSE322 · Class 1 · Introduction to Microprocessors
19
Component | What it does | Kitchen analogy
Program Counter (PC) | Holds the address of the next instruction. Increases by 1 after each fetch. | Bookmark in a recipe book
Instruction Register (IR) | Holds the current instruction while it is decoded and executed. | The step you are reading now
Accumulator (ACC) | Main working register: holds data used by the ALU and stores the ALU's result. | Your mixing bowl
ALU | Performs arithmetic/logic operations (in SAP-1: add and subtract). | The cook's hands
Memory | Stores the program's instructions and data (16 locations in SAP-1). | The recipe book and the pantry
Control Unit | Decodes the instruction and sends control signals to coordinate every step. | The head chef giving orders
Bus | Shared pathway that moves information between the components. | The shared kitchen counter
Learn the left two columns. The kitchen analogy is only a memory aid.

## Slide 20
PART 5 · SAP-1: A SIMPLE COMPUTER
How SAP-1 Executes an Instruction
CSE322 · Class 1 · Introduction to Microprocessors
20
FETCH
1
The PC holds the address of the next instruction.
2
The instruction is read from memory and travels over the bus.
3
It is placed in the Instruction Register (IR). The PC increases by 1.
DECODE
4
The Control Unit reads the IR and works out what to do.
EXECUTE
5
Required data is brought from memory over the bus.
6
The ALU and accumulator perform the operation.
7
The result is stored in the accumulator.
IR
CU
“This is an ADD”
Then the cycle repeats with the next instruction, which the PC is already pointing to.

## Slide 21
PART 5 · SAP-1: A SIMPLE COMPUTER
One Complete Example: ADD in SAP-1
CSE322 · Class 1 · Introduction to Microprocessors
21
Situation: the accumulator already holds 5. The next instruction, at address 1, is ADD 10: “add the value stored at address 10 to the accumulator”.
Address | Contents
0 | LDA 9 (done)
1 | ADD 10
2 | HLT
9 | 5
10 | 3
Memory
LDA = load accumulator
HLT = halt (stop)
FETCH
Memory [1] → IR
“ADD 10” is copied into the IR
DECODE
Control Unit
“add the value at address 10”
EXECUTE
Memory [10] → bus
the value 3 is sent to the ALU
EXECUTE
ALU / Accumulator
5 + 3 = 8
RESULT
Accumulator = 8
PC is now 2 (next: HLT)
REGISTERS: BEFORE → AFTER
 | Before | After
PC | 1 | 2
IR | LDA 9 | ADD 10
ACC | 5 | 8
Focus on the flow, not the circuitry:
fetch the instruction → decode it → get the data → compute → store the result.

## Slide 22
REVIEW
What Have We Learned?
CSE322 · Class 1 · Introduction to Microprocessors
22
Computer
CPU (processor)
ALU + Control Unit + Registers
Memory + Buses
Instructions
Fetch → Decode → Execute
SAP-1
Foundation for understanding 8086
5 key takeaways
1
The CPU executes instructions. A microprocessor is a CPU on a single chip.
2
A CPU has three core parts: the ALU (calculates), the Control Unit (coordinates) and registers (fast storage).
3
Memory holds instructions and data. Buses (data, address, control) carry information between the CPU and memory.
4
Every instruction goes through Fetch → Decode → Execute.
5
SAP-1 is a simple model of a CPU. The same ideas appear in the Intel 8086.

## Slide 23
REVIEW
Check Your Understanding
CSE322 · Class 1 · Introduction to Microprocessors
23
Q1
Which CPU component performs addition?
Q2
Where are instructions stored before they are executed?
Q3
What is the difference between an address and data?
Q4
What are the three stages of the instruction cycle, and what happens in each?
Q5
Why do we study SAP-1 before the 8086?
Try to answer from memory first, then check the slides. Discuss your answers with a classmate.

## Slide 24
COMING UP · CLASS 2
Next Class: Understanding the 8086
What is the 8086?
8086 architecture overview
BIU and EU (Bus Interface Unit, Execution Unit)
General-purpose registers
Segment registers
IP and FLAGS
Memory segmentation
Today's idea → in the 8086
Program Counter
→
Instruction Pointer (IP)
Accumulator
→
AX register
Registers
→
AX, BX, CX, DX, ...
ALU + Control Unit
→
Execution Unit (EU)
Bus + memory access
→
Bus Interface Unit (BIU)
Today we learned how a simple processor works. Next, we will see how these ideas appear in the Intel 8086.